1)
a) Identify the time intervals when TCP Slow Start is operating.
[1-6) and [23 - 26)

b) Identify the time intervals when TCP Congestion Avoidance is operating.
[6 – 22]

c) What is the value of ssthresh at the 4th transmission round?
Ssthresh = 32 as that is the cwnd that SS stops and CA starts

d) What is the value of ssthresh at the 10th transmission round?
No dup acks or timeouts have occurred so ssthresh = 32 still

e) What is the value of ssthresh at the 20th transmission round?
Had dup ack so ssthresh = cwnd/2 = 42/2 = 21

f) What is the value of ssthresh at the 24th transmission round?
Had timeout so ssthresh = cwnd/2 = 26/2 = 13

g) After the 16th transmission round, is the segment loss detected by a 3rd duplicate ACK or by a
timeout?
Is a 3rd dup ack as cwnd isn’t set to 1, rather cut in half.

h) Assuming a segment loss is detected after the 26th round by a timeout, what will be the values
of new congestion window size and ssthresh?
Cwnd = 1 and sshthresh = cwnd /2 = 4

2)

Time	Packet Received	Action Taken	List of unACKs packets	Total # dup ACKs	Estimated # outstanding packets	ssthresh value	cwnd size	cwnd range	# new packets to send	Notes
3 RTT	A5		5,6,7			4	4+1/4	5 - 8	1: #8
	A6		6,7,8			4	4+2/4	6 - 9	1: #9
	A7		7,8,9			4	4+3/4	7 -10	1: #10
	A8		8,9,10			4	5	8 -12	2: #11, #12	Lost #12
4 RTT	A9		9,10,11,12			4	5+1/5	9 -13	1: #13
	A10		10,11,12,13			4	5+2/5	10 - 14	1: #14	Lost #14
	A11		11,12,13,14			4	5+3/5	11 - 15	1: #15
	A12		12,13,14,15			4	5+4/5	12 -16	1: #16
5 RTT	Dup A12			1						From #13
	Dup A12			2						From #15
	Dup A12	Enter FR	12,13,14,15,16	3	5 – 3 = 2	2	2	12 - 13	None	From #16

6 RTT	A14		14, 15, 16	0	3	2	2	14 - 15	None

7 RTT	A17	Exit FR	None	0	0	2	2+1/2	17-18	#2: 17, 18